# Design
Sun (1 Y LED)
12 snowflakes (W LED)
3 snowman pieces (W LED)
color changing LED for sky?
(non-electrical):
Plexiglass on board with nails routing the shapes
Manhattan technique?
Used a recycled computer case side panel
13x11” window
2x2 snowflaxes
# Hardware
## MCU
Lowest cost STM32 (on digikey):
MCU only:
STMicroelectronics STM32F030K6T6
$1.32 @ 10
http://www.digikey.com/product-detail/en/STM32F030K6T6/497-14046-ND/4494296
2.4-3.6V

Atmel ATmega328P
1.8 – 5.5 V
Table X: Microcontrollers with GCC support
Manufacturer	Part #	Price	Core Processor	RAM, Flash (KB)	Voltage (V)	Package, I/O
Atmel	ATTINY48-AU	1.08*	AVR 12MHz	0.256, 4	1.8 – 5.5	32-TQFP (7x7), 28 I/O
	ATTINY88-AU-ND	1.116*		0.512, 8
Freescale Semiconductor - NXP	MKE02Z16VLC4-ND	1.173*	ARM Cortex-M0+ 40MHz	2, 16	2.7 – 5.5	32-LQFP (7x7), 28 I/O
STMicroelectronics	STM32F030K6T6	1.328*	ARM Cortex-M0 48MHz	4, 32	2.4 – 3.6	32-LQFP (7x7), 26 I/O

* @ quantity 10

Dev board:
STM32L100C-DISCO
$8.38
http://www.digikey.com/product-detail/en/STM32L100C-DISCO/497-13930-ND/4357642
1.65-3.6V
max: 120mA VDD/VSS (100 each), 80 all I/O (25 each)
Using an Atmel ATMega328p microcontroller because I have a few on hand.
## Power subsystem
USB
5V → 3.6V
5V → LED or pin→LED

Using a cheap 5V USB adapter connected to the MCU (which supports up to 5V). Used two capacitors between VCC and GND. Added three 30-Ohms resistors in parallel because cheap AC adapter provides 5.20V.